| No. | Parameters | Norm as per TR CU 013/2011 regarding ecological class 5 | Unit | Test method | Limits as per STB 1656-2016 | Actual value |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | min | max |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1. | RON | 80 | - | GOST 32339 | 92,0 | - | 92,4 |
| 2. | MON | 76 | - | GOST 32340 | 83,0 | - | 83,2 |
| 3. | Lead mass fraction | max 5* | mg/dm3 | GOST EN 237 | - | 5,0 | None |
| 4. | Density at 15 ºC | - | kg/m³ | STB ISO 3675 | 720,0 | 775,0 | 752,0 |
| 5. | Sulphur mass fraction | max 10 | mg/kg | GOST ISO 20846 | - | 10,0 | 6,0 |
| 6. | Oxidation stability | - | Min | STB ISO 7536 | 360 | - | more than 360 |
| 7. | Gum concentration (as washed with solvent) | - | mg/ 100 sm3 | STB ISO 6246 | - | 5 | 1 |
| 8. | Copper plate corrosion (3 hrs at 50 º C) | - | Class | STB ISO 2160 | Class 1 | Class 1 |
| 9. | Appearance | - | - | Visual control | Clear and transparent | Clear and transparent |
| 10. | Volume fraction of hydrocarbons: olefins, aromatics | max 18 max 35 | % | GOST ISO 22854 | - - | 18,0 35,0 | 14,1 32,3 |
| 11. | Benzene volume fraction | max 1 | % | GOST ISO 22854 | - | 1,0 | 0,60 |
| 12. | Oxygen mass fraction | max 2,7 | % | GOST ISO 12177 | - | 2,7 | 0,01 |
| 13. | Volume fraction of oxygenates: methanol ethanol isopropyl alcohol isobutyl alcohol tert-butyl alcohol ethers (5 and more C atoms)** other oxygenates | max 1* max 5 max 10 max 10 max 7 max 15 max 10 | % | GOST ISO 22854 | - - - - - - - | 1.0 5.0 10.0 10.0 7.0 15.0 10.0 | none 0.0 0.0 0.0 0.0 0,05 0.0 |
| 14. | Iron concentration | none | mg/dm3 | GOST 32514 | None | None |
| 15. | Manganese concentration | none | mg/dm3 | GOST 33158 | None | None |
| 16. | Volume fraction of monomethylaniline | none | % | GOST 32515 | None | None |
| 17. | Vapour pressure (VP) Class A Class B Class C and C1 Class D and D1 Class E and E1 Class F and F1 | 35-80 (summer) 35-100 (winter) | kPa | GOST EN 13016-1 | 45.0 45.0 50.0 60.0 65.0 70.0 | 60.0 70.0 80.0 90.0 95.0 100.0 | 52,6 |
| 18. | Volume fraction of evaporated gasoline at 70 ºC (E70): For classes A and B For classes C, C1, D, D1, E, E1, F, F1 | - | % | GOST ISO 3405 | 20.0 22.0 | 48.0 50.0 | 22,0 |
| 19. | Volume fraction of evaporated gasoline at 100 ºC (E100) | - | % |  | 46.0 | 71.0 | 46,0 |
| 20. | Volume fraction of evaporated gasoline at 150 ºC (E150) | - | % |  | 75.0 | - | 80,0 |
| 21. | Final boiling point (FBP) | - | ºC |  | - | 210 | 205 |
| 22. | Residue in a flask | - | % (vol.) |  | - | 2 | 1.0 |
| 23. | Vapour lock index (VLI) (10 VP +7 E70): Class C1 Class D1 Class E1 Class F1 | - | index | - | - - - - | 1050 1150 1200 1250 | - |

*for Russian Federation – none.

** components containing oxygen have not been used while gasoline production. According to the requirements of GOST ISO 22854 the value of 0,8% of the oxygenates volume fraction is considered as the absence of components containing oxygen.

Gasoline contains no additives.

Information on declaration of compliance: EAEU No. BY/112 11.01. TP013002 12490, valid till 22.06.2023.

Conclusion: product corresponds to the requirements of STB 1656-2016 and Technical Regulation of Customs Union 013/2011 as regard ecological class K5.

Guarantee period – 1 year from the production date.

Chemist: Y.A. Ilyina                                        Date of passport issue: 21.07.2020