PASSPORT No 1662

OJSC “NAFTAN”, NOVOPOLOTSK

FUEL OIL

GOST 10585-2013

Grade: fuel oil 100, 3,0 %, ashy, with setting  point 25 ºС

Production date: 06.08.2016

Tank 419

Registration number of sample: 38677

Net weight:  3805 tons

Lot number:   1662

| № | Parameters | TR CU 013/2011 | GOST 10585-2013 | Factual | Test methods |
| --- | --- | --- | --- | --- | --- |
| 1. | Viscosity at 100°С, max, redwood, degrees BY | - | 6,8 | 5,65 | GOST 6258-85 |
| 2. | Ash, %, max | - | 0,14 | 0,0520 | GOST 1461-75 |
| 3. | Mechanical impurities content, mass fraction, %, max | - | 1,0 | 0,0560 | GOST 6370-83 |
| 4. | Water content, mass fraction, %, max | - | 1,0 | 0,7 | GOST 2477-65 |
| 5. | Water-soluble acids and alkalies content | - | none | none | GOST 6307-75 |
| 6. | Sulfur content, mass fraction, %, max | 3,5 | 3,0 | 2,82 | STB 1420-2003 |
| 7. | Open cup flash point, °С, min | 90 | 110 | 114 | GOST 4333-87 |
| 8. | Pour point °С, max | - | 25 | 9 | GOST 20287-91 Method B |
| 9. | Combustion heat (lowest) given in solid fuel (no rejected), kJ/kg, min | - | 39 900 | 40 450 | GOST 21261-91 |
| 10. | Density at 15°C, kg/m3 | - | No standard | 991,4 | GOST 31072-2002 |

Information about additive: no additives.

Declaration of conformity: №  ТС BY/112 11.01. TP013 002 03764, valid until 31.03.2021

Conclusion: the product conforms to GOST 10585-13 and TR CU 013/2011 requirements.

Guarantee period of keeping – 5 years from a date of production.