Продукт остаточный гидрокрекинга

| № | Показатель | Норма |
| --- | --- | --- |
| 1 | Плотность при 20°С, кг/м3 | Не выше 900,0 |
| 2 | Плотность при 15°С, кг/м3 | Не выше 910,0 |
| 3 | Темп-ра вспышки в отк. тиг, °С |  |
| 4 | Температура застывания, °С | Не выше 40 |
| 5 | Температура начала кипения, °С | Не ниже 230 |
| 6 | 50% выкипает при t, °С | диапазон 370 - 435 |
| 7 | Коксуемость, % | не более 0,10 |
| 8 | Массовая доля ванадия, % | не более 0,0001 |
| 9 | Содержание воды, % м. | не более 0,5 |
| 10 | Содержание серы, % | не более 0,0400 |
| 11 | Цвет, единицы ЦНТ | не более 6,0 |

PRODUCT RESIDUE OF HYDROCRACKING

| No | Parameters | Requirements according to TRLA |
| --- | --- | --- |
| 1. | Density at 20ºC, kg\m3, max | 900 |
| 2. | Density at 15ºC, kg\m3, max | 910 |
| 3. | Flash point defined in an open cup, ºC | Not defined |
| 4. | Temperature of solidification, ºC, max | 40 |
| 5. | Distillation: a)temperature of distillation beginning, ºC, min b) 50% distilled at temperature, ºC, limits | 230 370-435 |
| 6. | Coking power, % vol, max | 0,1 |
| 7. | Vanadium contents, %, max | 0,0001 |
| 8. | Water contents, % max | 0,5 |
| 9. | Sulfur content. % max | 0,04 |
| 10 | Color, units of CNT, max | 6,0 |