PASSPORT No 2062

OJSC “NAFTAN”, NOVOPOLOTSK

FUEL OIL

GOST 10585-2013

Grade: fuel oil 100, 3,0 %, ashy, with setting  point 25 ºС

Production date 01.08.2018

Tank 420

Registration number of sample: 34551

Net weight: 3503 tons

Lot number: 2062

| № | Parameters | TR CU 013/2011 | GOST 10585-2013 | Factual | Test methods |
| --- | --- | --- | --- | --- | --- |
| 1. | Viscosity at 100°С, max, redwood, degrees BY | - | 6,8 | 6,2 | GOST 6258-85 |
| 2. | Ash, %, max | - | 0,14 | 0,0510 | GOST 1461-75 |
| 3. | Mechanical impurities content, mass fraction, %, max | - | 1,0 | 0,060 | GOST 6370-83 |
| 4. | Water content, mass fraction, %, max | - | 1,0 | 0,7 | GOST 2477-2014 |
| 5. | Water-soluble acids and alkalies content | - | none | none | GOST 6307-75 and p.7.5 GOST 10585-2013 |
| 6. | Sulfur content, mass fraction, %, max | 3,5 | 3,0 | 2,93 | STB 1420-2003 |
| 7. | Open cup flash point, °С, min | 90 | 110 | 174 | GOST 4333-2014 |
| 8. | Pour point °С, max | - | 25 | 9 | GOST 20287-91 Method B |
| 9. | Combustion heat (lowest) given in solid fuel (no rejected), kJ/kg, min | - | 39 900 | 40 351 | GOST 21261-91 |
| 10. | Density at 15°C, kg/m3 | - | No standard | 977,3 | GOST 31072-2002 |
| 11. | Initial boiling point, °С, min | - | 200,0 | 229,0 | ASTM D 86-12 |
| 12. | Closed cup flash point, °С, min | - | 80 | 100 | ASTM D 93-13 |

Information about additive: no additives.

Declaration of conformity: №  ТС BY/112 11.01. TP013 002 03764, valid until 31.03.2021

Conclusion: the product conforms to GOST 10585-13 and TR CU 013/2011 requirements.

Parameters 11, 12 determine in supply of fuel oil for exports.

Guarantee period of keeping – 5 years from a date of production.