OJSC Mozyr OR

PASSPORT No 804

Diesel Fuel DT-L-K5 grade C

STB 1658-2015

Lot №: 804

Production date  03.07.2017                Tank № 115                           Innage: 1300 sm

| Parameters | Units | Norm as per TR CU 013/2011 for ecological class 5 | Test method | Value as per STB 1658-2015 | Actual value |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Min | Max |  |
| 1. Cetane number | - | Min 51 | GOST ISO 5165 | 51,0 | - | 51,2 |
| 2. Cetane index | - | - | STB ISO 4264 | 46,0 | - | 54,5 |
| 3.Density at 15 ºC | kg/m³ | - | STB ISO 12185 | 820,0 | 845,0 | 829,6 |
| 4. Mass fraction of polycyclic aromatic hydrocarbons | % (m/m) | max 8 | GOST ЕN 12916 | - | 8,0 | 0,4 |
| 5. Sulphur content | mg/kg | max 10 | GOST ISO 20846 | - | 10,0 | 7,3 |
| 6. Flash point in closed cup | ºC | min 55 | STB ISO 2719 | above 55 | - | 74 |
| 7. Coking power ( on 10% residue) | % (m/m) | - | GOST ISO 10370 | - | 0,30 | 0,01 |
| 8. Ash content | % (m/m) | - | STB ISO 6245 | - | 0,01 | 0,001 |
| 9. Water content | mg/kg | - | STB ISO 12937 | - | 200 | 45 |
| 10. Content of mechanical impurities | mg/kg |  | STB ЕN 12662 | - | 24 | 12,0 |
| 11. Copper plate testing (3 hrs at 50 ºC) | сlass | - | STB ISO 2160 | Class 1 | Class 1 |
| 12. Oxidation stability | g/m³ | - | STB ISO 12205 | - | 25 | 12,0 |
| 13. Lubricity, wear scar diameter (WSD 1,4) at 60 ºC | micron | max 460 | GOST ISO 12156-1 | - | 460 | 416 |
| 14. Viscosity at 40 ºC | mm²/s | - | STB ISO 3104 | 2,000 | 4,500 | 2,734 |
| 15. Distillation: - Distilled at 250 ºC - Distilled at 350 ºC - 95 %(V/V) distilled at temperature | % vol. ºC | - - max 360 | GOST ISO 3405 | - 85 - | less 65 - 360 | 39,3 95,9 346,5 |
| 16. Cold filter plugging point | ºC | - | GOST ЕN 116 | - | minus 5 | minus 7 |

Information about additives: lubricating additive contains; no metal-containing additives.

Information on declaration of compliance: № TC BY/112 11.01. TP013 002 03564, valid till 21.02.2019.

Conclusion: standart product corresponds to the requirements of STB 1658-2015 and TR CU 013/2011 as to ecological class 5.

Guarantee period – 1 year from production date.