JSC Mozyr OR

Passport No 998

Unleaded Gasoline AI-92-K5-Euro under STB 1656-2016 Class B

Lot №: 998                      Tank № 110         Innage  1600 sm                                                        Production date: 10.07.2019

| № | Parameters | Norm as per TR CU 013/2011 regarding ecological class 5 | Unit | Test method | Limits as per STB 1656-2016 | Factual value |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | min | max |  |
| 1. | RON | 80 | - | GOST 32339 | 92,0 | - | 92,3 |
| 2. | MON | 76 | - | GOST 32340 | 83,0 | - | 83,5 |
| 3. | Lead mass fraction | max 5* | mg/dm3 | GOST EN 237 | - | 5,0 | None |
| 4. | Density at 15 ºC | - | kg/m³ | STB ISO 3675 | 720,0 | 775,0 | 748,0 |
| 5. | Sulphur mass fraction | max 10 | mg/kg | GOST ISO 20846 | - | 10,0 | 8,0 |
| 6. | Oxidation stability | - | min | STB ISO 7536 | 360 | - | more 360 |
| 7. | Gum concentration (as washed with solvent) | - | mg/ 100 sm3 | STB ISO 6246 | - | 5 | 1 |
| 8. | Copper plate corrosion (3 hrs at 50 º C) | - | Class | STB ISO 2160 | Class 1 | Class 1 |
| 9. | Appearance | - | - | Visual control | Clear and transparent | Clear and transparent |
| 10. | Volume fraction of hydrocarbons: olefins aromatics | max 18 max 35 | % | GOST ISO 22854 | - - | 18,0 35,0 | 13,2 33,3 |
| 11. | Benzene volume fraction | max 1 | % | GOST ISO 22854 | - | 1,0 | 0,76 |
| 12. | Oxygen mass fraction | max 2,7 | % | GOST ISO 22854 | - | 2,7 | 0,29 |
| 13. | Volume fraction of oxygenates: methanol ethanol isopropyl alcohol isobutyl alcohol tert-butyl alcohol ethers (5 and more C atoms)** other oxygenates | max 1* max 5 max 10 max 10 max 7 max 15 max 10 | % | GOST ISO 22854 | - - - - - - - | 1,0 5,0 10,0 10,0 7,0 15,0 10,0 | none 0.0 0.0 0.0 0.0 1,80 0,0 |
| 14. | Iron concentration | none | mg/dm3 | GOST 32514 | none | none |
| 15. | Manganese concentration | none | mg/dm3 | GOST R 51925 | none | none |
| 16. | Volume fraction of monomethylaniline | none | % | GOST 32515 | none | none |
| 17. | Vapour pressure (VP) Class A Class B Class C and C1 Class D and D1 Class E and E1 Class F and F1 | 35-80 (summer) 35-100 (winter) | kPa | STB EN 13016-1 | 45,0 45,0 50,0 60,0 65,0 70,0 | 60,0 70,0 80,0 90,0 95,0 100,0 | 55,3 |
| 18. | Volume fraction of evaporated gasoline at 70 ºC (E70): For classes A and B For classes C, C1, D, D1, E, E1, F, F1 | - | % (V/V) | GOST ISO 3405 | 20,0 22,0 | 48,0 50,0 | 25,6 |
| 19. | Volume fraction of evaporated gasoline at 100 ºC (E100) | - | % (V/V) |  | 46,0 | 71,0 | 48,5 |
| 20. | Volume fraction of evaporated gasoline at 150 ºC (E150) | - | % (V/V) |  | 75,0 | - | 79,7 |
| 21. | Final boiling point (FBP) | - | ºC |  | - | 210 | 208 |
| 22. | Residue in a flask | - | % (V/V) |  | - | 2 | 1,0 |
| 23. | Vapour lock index (VLI) (10 VP +7 E70): Class C1 Class D1 Class E1 Class F1 | - | index | - | - - - - | 1050 1150 1200 1250 | - |

*for Russian Federation – none.

** with tert-amyl methyl ether and C7 ether.

Gasoline contains no additives. Information on declaration of compliance: EUU № BY/112 11.01. TP013 002 06595, valid  till 29.06.2020.

Conclusion: product corresponds to the requirements of STB 1656-2016 and Technical Regulation of Customs Union 013/2011 as regard ecological class 5.

Guarantee period – 1 year from production date.