OJSC Mozyr Refinery

Passport No 556

Gasoline unleaded AI-92-K5-Euro

Specification STB 1656-2011

Production date 14.05.2017

| # | Description | Method of testing | Limit value Under STB 1656-2011 | Actual value |
| --- | --- | --- | --- | --- |
| 1 | Density at 15 º C, kg\m³, max | STB ISO 3675 | 720,0 – 775,0 | 747,0 |
| 2 | Research Octane Number, min Motor Octane Number, min | STB ISO 5164 STB ISO 5163 | Min 92,0 Min 83,0 | 92,4 83,8 |
| 3 | Lead concentration, mg\dm³, max | STB ЕН 237 | Max 5,0 | Abs. |
| 4 | Volume fraction of evaporated gasoline at 70 º C (E70), % (V/V) For classes A and B For classes C, C1, D, D1, E, E1, F, F1 Volume fraction of evaporated gasoline at 100 º C (E100), % (V/V) Volume fraction of evaporated gasoline at 150 º C (E150), % (V/V) Final boiling point, º C Residue in a flask,% (V/V) | STB ISO 3405 | 20-48 22-50 46-71 min. 75 max. 210 max. 2 | 25,6 49,1 81,5 208 1,0 |
| 5 | Reid Vapor Pressure , kPa, RVP For class A For class B For classes C and C1 For classes D and D1 For classes E and E1 For classes F and F1 | STB EN 13016-1 | 45-60 45-70 50-80 60-90 65-95 70-100 | 53,70 |
| 6 | Existent gum, mg per 100 sm³ of gasoline, max | STB ISO 6246 | 5 | 1,0 |
| 7 | Oxidation stability, minutes, min | STB ISO 7536 | 360 | More than 360 |
| 8 | Sulfur mass fraction, mg/kg max | STB ISO 20846 | Max 10 | 7,2 |
| 9 | Copper test (3 hours at 50 º C) | STB ISO 2160 | Class 1 | Class 1 |
| 10 | Volume ratio of benzene, %, max | STB ЕН 12177 | Max 1,0 | 0,62 |
| 11 | Volume ratio of hydrocarbons, %, max: olefins aromatic | STB ЕН 22854 | Max 18 Max 35 | 8,9 33,6 |
| 12 | Oxygen mass fraction, %, max | STB ЕН 22854 | Max 2,7 | 0,55 |
| 13 | Volume fraction of oxygenates, %, max: - methanol - ethanol - isopropyl alcohol - isobutyl alcohol - tret- butyl alcohol - ethers (five and more atoms of carbon) - other oxygenates | STB ISO 22854 | 1,00 5,00 10,00 10,00 7,00 15,00 10,00 | Abs 0,00 0,00 0,00 0,00 3,57 0,00 |
| 14 | Existent gum (flushed out by resolvent), mg/100 ml | STB ISO 6246 | Max 5 | 1 |
| 15 | Appearance | Visual control | Transparent and Clean | Transparent and Clean |
| 16 | Ferrum concentration, mg/l | GOST 32514 | Abs | Abs |
| 17 | Manganese concentration, mg/l | GOST P 51925 | Abs | Abs |
| 18 | Volume fraction of toluidine,% | GOST P 54323 | Abs | Abs |