APPENDIX 1

Propane-butane automotive

| No | Parameters | Requirements according to TRLA | Testing method |
| --- | --- | --- | --- |
| 1. | Motor octane number (MON), min | 89,0 | STB EN 589-2008 attachment B |
| 2. | Mass. fraction of components, wt %: | - | GOST 10679-76 |
|  | sum of methane, ethane and ethylene | - |  |
|  | propane | 40,0 - 60,0 |  |
|  | propylene | - |  |
|  | isobutane | - |  |
|  | butane normal | - |  |
|  | sum of butylene | - |  |
|  | sum of C5 hydrocarbons and above | - |  |
| 3. | Sum of unsaturated hydrocarbons, max | 6,0 | GOST 10679-76 |
| 4. | Liquid residue at 20 ºC, vol %, max | 1,6 | p.8.2 STB 2262-2012 |
| 5. | Excess vapour pressure, at the temperature of plus 45 ºC, MPa, max | 1,6 | GOST 28656-90 |
| 6. | Excess vapour pressure, at the temperature of minus 20 ºC, MPa, min * | 0,07 | GOST 28656-90 |
| 7. | Hydrogen sulfide and mercaptan sulfur, %, max | 0,035 | GOST 22985-90 |
|  | including hydrogen sulfide, max | 0,003 | GOST 11382-76 |
| 8. | Free water and caustic content | Abs. | p.8.2 STB 2262-2012 |
| 9. | Density at 20ºC, kg/m3 | - | GOST 28656-90 |
| 10. | Density at 15ºC, kg/m3 | - | GOST 28656-90 |
| 11. | Copper strip corrosion (1 h at 40 ºC) | Class 1 | GOST ISO 6251-2013 |

*Excess vapour pressure at the temperature of minus 20 ºC is determined in winter period of time